## Slide 1: Identify Hard Stop and Momentary Stop Using Vehicle Trajectory Dataset CSE623: Machine Learning School of Engineering and Applied Science, Ahmedabad University
Team: TechTitans
Megh Patel | Devanshi Pathak | Dharmi Vekariya | Konark Karia
AU2544020 | AU2544014 | AU2544029 | AU2544011

## Slide 2: Problem Statement
Traffic intersections present complex vehicle behaviors — especially hard stops, where vehicles abruptly halt or remain stationary for extended durations.
These events can indicate emergencies, illegal parking, or traffic anomalies.
Build a binary classifier to detect Hard Stops vs. Normal Motion using UAV-captured vehicle trajectory data.
Simplify from multi-class to binary classification for better precision and practicality.
Challenge
Our Objective

## Slide 3: Literature Review
Combines Dijkstra algorithm with machine learning models (Random Forest, XGBoost, GA-RF)
Aims to improve traffic management at urban intersections
Performs vehicle classification and trajectory prediction
Uses simulated traffic data for evaluation
GA-RF model shows highest accuracy and reliability
Better handles complex and dynamic traffic conditions than traditional models
“An optimized hybrid approach for trajectory prediction and vehicle classification at intersections using Dijkstra and Random Forest enhanced by a Genetic Algorithm”

## Slide 4: Methodology | Dataset & Feature Engineering
Dataset Features
xc, yc | Spatial coordinates (X & Y)
w, h | Bounding box dimensions
Org vel / Smoothed vel | Original & smoothed velocity (kmph)
SD(m) | Standard deviation of motion
FlightHeight | UAV altitude
Acceleration | Engineered: velocity delta over time
Preprocessing Pipeline
1
Load & merge multi-file UAV CSV trajectory data
2
Drop rows with null values (Org dir, Smoothed dir)
3
Engineer acceleration from velocity differences
4
MinMax scale all numeric features → [0, 1]
5
Binary label: velocity < 90 kmph → Hard Stop (1)
6
80/20 Train-Test split with stratification

## Slide 5: Methodology | Model & Classification
Why Random Forest?
Structured Data
Tree-based models excel on tabular/structured data
Non-linear
Captures non-linear feature relationships without tuning
Anti-Overfitting
Ensemble of trees reduces variance and overfitting
Label Generation (Threshold = 90 kmph)
Class 0 (Normal Motion)
Velocity ≥ 90 kmph → vehicle in normal motion Class 1 (Hard Stop)
Velocity < 90 kmph → stationary or abrupt halt
Class Distribution

## Slide 6: Results & Evaluation
Key Insight
Random Forest outperformed with 98.74% accuracy on structured tabular data. Minimal falase alarms (Precision=1.00) prevents erroneous emergency triggers
0.90
F1-Score (Hard Stop)
98.74%
Overall Accuracy
Classification Report
0.99
Precision (Hard Stop)
0.82
Recall (Hard Stop)
Class | Precision | Recall | F1-Score | Support
Normal Motion (0) | 0.99 | 1.00 | 0.99 | 72,462
Hard Stop (1) | 0.99 | 0.82 | 0.90 | 5,232
Weighted Avg | 0.99 | 0.99 | 0.99 | 77,694

## Slide 7: Future Scope
Data Balancing
Address class imbalance (72K vs 5K) using SMOTE or class-weighted training to improve recall for hard stop events.
Adaptive Threshold
Replace fixed 90 kmph velocity threshold with data-driven or dynamic labeling to reduce dependency on arbitrary cutoffs.
Model Ensemble Method
Experiment with Gradient Boosting (XGBoost, LightGBM) or stacked ensembles for potential further accuracy gains.
Real-time Integration with YOLO
Connect the classifier to live UAV video streams via YOLO object detection for real-time hard stop detection in traffic.

## Slide 8: References
Chouiekh, C., Yahyaouy, A., Sabri, M. A., & Karmouni, H. (2025).
An optimized hybrid approach for trajectory prediction and vehicle classification at intersections using Dijkstra and random forest enhanced by a genetic algorithm. Franklin Open, 100445.